## Slide 1: A SDN-based HoneyGrid

## Slide 2: HoneyGrid Goals (cont.)
2. Distributed Resources Management through DLB NFV
  Deploying honeynets at multiple locations is not novel, but existing approaches either are not resource-efficient or have scalable issues.
  Centralize the management honeynet resources scattered over the world.
  Allow honeynets to join/exit dynamically.
  Allow resource allocation policies to get dynamically updated.

## Slide 3: HoneyGrid Goals (cont.)
3. Support NFV apps to update policy
  It’s hard to propose a honeynet to have all functionalities, our honeygrid should be extensible, supporting any 3-rd party implemented NFVs (e.g., IDS) to specify policies (containment policy, resource allocation policy, consistency policy )

## Slide 4: HoneyGrid Goals
1. HIH and LIH combination.
  Allocating each src to a single High-interaction Honeypot (HIH) requires unaffordable resources (/17 network, 5 min for each VM, 700 VMs are required)
  Low-interaction Honeypot (LIH) can only emulate limited functions and can be recognized by attacker.
  Migrate flow from LIH to HIH when necessary. (~80% traffic are scanning traffic)
  Fast detect idle high-interaction honeypot (HIH) to revert for another flow.

## Slide 5: A SDN-based HoneyGrid
Protocol-independent flow migration engine.
  Automatically generate LIH (RolePlayer, ScriptGen)
  Modify OpenvSwitch to support seq number and ack number modification.
Combing idle timeout and hard timeout to optimize HIH usage.
Resource manager
  allocate resource for each flow
    Default:
      1). HIH, local VM have high priority
      2). One-src-one-dst per VM
    Support more advanced policy
  Monitor and manage newly added and obsolete resources.
Asynchronous trace analyzer (3-rd party app)
Containment policy generator (3-rd party app GQ)

## Slide 6: Architecture

## Slide 7: Example: Telnet Migration
Notes: Controller assign LIH to respond new telnet traffic ((1) and flow 1).
If an attacker tries to execute cmd after login, telnet responder in LIH asks controller if the attacker can be responded by HIH (2).
Controller finds an available VM, so it tells HIH the VM gets new job (3), delete flow1 and add new flows (flow2)

## Slide 8: Controller & HIH Manager Communication (normal exit)
On step (3), controller tells manager HIH3 will be assigned to a client and sets a timeout (5 mins by default).
When timeout event gets triggered, manager sends an NA msg to controller (4) and starts to revert HIH3 (7). When the HIH gets running with a clean state, manager sends a free msg to controller (8).
When receiving a NA msg, controller deletes existing flows for that HIH; Controller also needs to update HIH table when receiving msgs from manager (2,5,9).

## Slide 9: Controller & HIH Manager Communication (early exit)
On step (1), add flow rule with a short idle timeout.
Controller listens to idle timeout event (4) and updates HIH table. If the number of flows becomes zero, Controller sends revert msg (5) to HIH manager.

## Slide 10: Evaluation
1. Daily traffic analysis (traffic analyzer)
  Tags for popular ports
  Per source report
  Captured binaries report
2. Flow migration
  Video demonstration
  Effectiveness analysis (percentage of scanning traffic)
3. HIH management
  Average alive time for HIH flow and VM
  Longest alive time for HIH flow

## Slide 11: Evaluation (cont.)
4. Src priority assignment
  3rd-party programs (e.g. traffic analyzer) informing controller interesting src IPs.
  Increase of captured data after enabling src priority
5. Throughput with/without load balancer
6. Global distribution
  Traffic difference among HoneyNets in different countries
  Throughput for flows entering into honeynet in country A but responded by honeypots located in country B.