## Slide 1: RuleTris: Minimizing Rule Update Latency for TCAM-based SDN Switches
Xitao Wen*, Bo Yang#, Yan Chen*, Li Erran Li$, Kai Bu#, Peng Zheng&, Yang Yang*, Chengchen Hu&
*Northwestern University, #Zhejiang University, $Fudan University, &Xi’an Jiaotong University
Notes: Let’s dive into the first work

## Slide 2: Motivation
Flow table update bottleneck
  Limitation of TCAM (Ternary Content-Addressable Memory)
  10s to 100s of rule operations per second
Existing controllers generate inflated flow table updates
  Unnecessary priority updates
  Massive TCAM internal moves
Ultimate Goal: minimizing TCAM update operations to speed up updating
  Only update the “diff”
Notes: FT update is bottleneck to network dynamics. HW limitation, SDN switches process 10s-100s rule updates per second. Unlikely to improve. So, strong incentive to minimize…
How rule updates are generated
SDN modules generate policies in languages. Policy compiler translates static policy to prioritized flowtable. We’d like to have update gen, which compares FTs and update diff

## Slide 3: Motivating Example
Update schedule with priority clue
  1 rule adds + 4 rule moves

## Slide 4: Motivating Example (cont.)
Update schedule with dependency graph
  1 rule adds + 2 rule moves
Such redundant moves contribute over 95% in average!

## Slide 5: Key Insight
Dependency Graph (DAG) provides two optimality guarantees
Minimum size flow table
Minimum number of TCAM moves for table update

## Slide 6: Challenges
Speed, speed, speed!
How to efficiently generate DAG?
  O(n2) algorithm to obtain DAG from scratch
  Usually takes minutes for a thousand rules
How to efficiently optimize updates with DAG?
  Slow processor, limited memory on switches

## Slide 7: RuleTris Architecture
Front-end in controller
  An incremental SDN policy compiler that preserves DAG
Back-end in switch firmware
  Redundancy Eliminator, Update Scheduler…
F/B Interface
  Flow table + DAG

## Slide 8: Front-end
How to efficiently generate DAG?
Our approach
  Track DAG along with flow table compilation
  Linear additional time complexity!
Will provide background on composition compiler first

## Slide 9: A Bit More Background
Match | Action
Match | Action
Match | Action
+
>>
)
(
Compilers use the composition conﬁguration to guide the recursive composition compilation.

## Slide 10: Background: Flow Table Composition
Combine multiple flow tables into one functional equivalent flow table
Two operators: parallel, sequential
Parallel of Monitor and Route
Sequential of LB and Route

## Slide 11: Background: Composition Compiler without DAG
Compile multiple flow tables into a single flow table
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
Priority
Match
Action

## Slide 12: Background: Composition Compiler without DAG
Compile multiple flow tables into a single flow table
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)

## Slide 13: Background: Composition Compiler without DAG
Compile multiple flow tables into a single flow table
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
9. srcip=1.0.0.0/24  count
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop

## Slide 14: RuleTris Composition Compiler
A generic composition compiler which features
DAG preservation during composition
  Parallel
  Sequential
Efficient incremental compilation (see the paper)

## Slide 15: DAG Preservation for Parallel Composition
Infer dependency relations via graph cross product
Then eliminate those with empty match

## Slide 16: DAG Preservation for Parallel Composition (cont’d)
Special treatment for redundant rules

## Slide 17: DAG Preservation for Sequential Composition

## Slide 18: Optimality Guarantee
We proved that RuleTris front-end generates optimal DAG that is both complete and minimum
(see the paper for the proof).

## Slide 19: Back-end
Update Scheduler
  Given delta flow table and delta DAG
  Calculate the update schedule with minimum number of TCAM moves
Redundancy Eliminator
CacheFlow Manager

## Slide 20: Update Scheduler
Rule Insertion
  Step 1: Find TCAM location range for the inserted rule
  Step 2: Find nearest upper slot and lower slot
  Step 3: Search for shortest moving chain upwards and downwards
  Step 4: Use the shorter path for actual update
Shortest Moving Chain Searching
  Dynamic programming
Notes: J -> D -> A
J -> E -> F
Dynamic programming: Iterative searching bounded by # of slots in between

## Slide 21: Implementation
RuleTris front-end
  Stand-alone composition compiler
  5K lines of Java code
  Interface with open-source Ryu controller
RuleTris back-end
  Implemented in firmware of an FPGA-based hardware switch, ONetSwitch
  3K lines of C code
Front-end/back-end communication
  Extension to OpenFlow protocol for carrying DAG and DAG updates

## Slide 22: Evaluation Results
Compare with two priority based approaches
  Baseline
  CoVisor [NSDI 2015]: incremental update
Experiment 1: Parallel composition
Rule update overhead of L3-L4 monitoring + L3 router.
Notes: Methodology: Small hardware, Large emulation
Metrics: Compilation time, Firmware time, TCAM update time
Comparison: Baseline, priority-based non-incremental compiler + original firmware
  CoVisor, priority-based incremental compiler + original firmware
  RuleTris

## Slide 23: Evaluation Results II
Experiment 2: Sequential composition
Rule update overhead of L3-L4 NAT > L3 router.
RuleTris achieves a median of <12ms and 90-percentile of <15ms for the per-rule update latency
Outperform even CoVisor deployed on the same hardware switch by ∼20x.

## Slide 24: Conclusions
RuleTris is a novel SDN policy update optimization framework
It minimizes rule update latency for TCAM-based SDN switches
See our SDN related work at
http://list.cs.northwestern.edu/sdn
Thanks!