## Slide 1: Delay-tolerant networking
S. Burleigh, A. Hoke, L. Torgerson, K. Fall, V. Cerf, B. Durst, K. Scott, H. Weiss
An approach to Interplanetary Internet
Presented by Fabián E. Bustamante

## Slide 2: Upgrading a Martian’s weather station software
Deep space R/F link, with CFDP-RP link ARQ
Relay orbiter 2
Relay orbiter 1
Weather station
Antenna complex
Workstation
A scientist needs to upgrade the software in a weather stations’ data management computer.
The module must be xfer from the scientist’s workstation to a deep antenna complex to a constellation of relay satellites in low Mars orbit to the weather station

## Slide 3: Internet and Deep-space
TCP/IP over Internet
  Relatively small signal propagation delays (milliseconds)
  Relatively high data rates
  Bidirectional communications always
  Continuous end-to-end connectivity
  On-demand network access with high potential for congestion
Communication in deep space
  Very large signal propagation latencies (minutes)
  Relatively low data rates (8-256 kb/s)
  Time-disjoint periods of reception/transmission
  Intermittent scheduled connectivity
  Centrally managed access to the communication channel w/ essentially no potential for congestion

## Slide 4: CCSDS & its File Delivery Protocol (CFDP)
Consultative Committee for Space Data Systems (CCSDS)
  Introduced a number of standards for deep space communication
CFDP – reliable FT across interplanetary distances
  To deal with high latencies in CFDP
    Time to establish a connection > communication opportunity – no connection protocol, but managed communication parameters
    RTT >> time to transmit file – don’t wait for ACKs
    Large number of concurrent file transfers – keep retransmission buffers in stable storage
  Not suitable stack works well for end-to-end use

## Slide 5: Why not the Internet protocols?
Reliable transport – many applications need reliable transfers
  Issues with TCP
    Sender and receiver must negotiate a connection – this requires a least one round-trip before application data can be sent
    TCP delivers received data in transmission order, any data loss requiring retransmission will delay delivery of all subsequent data transmitted
    TCP throughput drops as RTT increases

## Slide 6: Why not the Internet protocols?
Issues with TCP
  TCP transmission is end-to-end, an issue when the links involved are quite different
  Consider a three hop route
  For retransmission, A must keep copy of messages until is sure retransmission is not necessary
    If end-to-end – A must retain msgs for 961,200 ms
    If hop-by-hop, 1000ms (500ms x 2)
    And think of the buffer space needed!
UDP
  You will have to re-invent retransmission
A
B
C
D
500ms
100ms
8min
One-way signal propagation delay

## Slide 7: Delay-Tolerant Network architecture
DTN
  Use the best suited protocols at each layer
  Add a new overlay layer bet/ application and locally optimized protocols
  Overlay acts as application-level gateway, offering and end-to-end transmission service that is reliable & efficient
The design of the overlay cannot assume
  Continuous connectivity
  Low or constant transmission latency
  Low error rate or low congestion
  High transmission rate or symmetrical data rates
  Common name or address expression syntax/semantics
  In-order data arrival
… but should take advantage of any if available

## Slide 8: DTN fundamental principles
A postal model of communication
  Arbitrary transmission latencies – no conversational interchange
  E.g. to transfer a file, bundle together in one message everything you need (requesting user’s name and password, name of the file, encoding instructions, etc)
  Bundles ~ functionally similar to email messages
Tiered functionality
  Bundling protocol performs any additional function that the locally optimized protocol can’t
Terseness
  Aim at low bandwidth usage even at the price of processing complexity

## Slide 9: DTN main structural elements
Tiered forwarding
  DTN nodes in a region use the locally optimized protocol
  Forwarding of bundles among DTN nodes in != regions is performed by Bundling through gateway nodes
    Gateway nodes – nodes with I/F in each adjacent region
  Bundling’s store-and-forward operation may require long deferred transmissions
Tiered naming and addressing
  Destination identifier of a bundle must map to an address in the destination address space
  But we need a region identifier to route at the bundling layer
  {region ID, regional destination id}
    Regional destination id are late bound

## Slide 10: DTN main structural elements
Six DTN nodes within three regions; each node has an I/F for each region within which it operates
{X, a}
{Z,a}
{Z,d}
{Y,b} {Z, c}
{Y, c}
{X, b} {Y, a} {Z, b}
Region X
Region Y
Region Z

## Slide 11: DTN main structural elements
Tiered routing
  Route computation at the bundling layer must be sensitive to new link opportunities or contacts
    Maybe scheduled – manually or automated
    Discoverable in real time
    Predictable – mobility patterns or orbital dynamics
    Stochastically computed – based on prior contact history
Tiered automatic retransmission
  Regional retransmission is the most efficient
  Still, to handle regions with long RTTs, Bundling supports custodial retransmission – a node takes custody of a bundle (keeping a copy) until a downstream node takes over it

## Slide 12: DTN main structural elements
Tiered security
  If necessary, exchange of bundles between adjacent nodes may be subject to verification of cryptographic credentials
  The certificate must travel with the bundle, however, and it may be too large considering the terseness principle
Tiered congestion control
  DTN relies on regional measures, either protocol-based or reservation/management based

## Slide 13: DTN main structural elements
Resilient delivery
  Ultimate source and destinations are service agents (processes, threads, …)
  End-to-end latency may be so long that agent is off when bundle arrives
    Keep a copy for deferred delivery
    Potentially reanimate the agent for delivery
Postal service level
  QoS levels based on the US Postal service
  Three levels of priority: low, standard, high
  Three postal service notifications
    Notice of initial transmission (notice of mailing)
    Notice of delivery to ultimate destination (return receipt)
    Report of route taken (delivery record)

## Slide 14: Final comments
Building DNT to work within UDP/IP, without bundling
  Familiar to application developers
  Split of bundling functionality is too messy, fragile and costly
Interplanetary Internet → Generalized DTN
  Research group on DTN as part of the Internet Research Task Force
    http://www.dtnrg.org/wiki
  Prototype implementation build by guys at Berkeley; later release v2.5.0, Oct. 2007