# MSIT 458 Homework 7

Notes:		1. To be done by each group.

2. Please do not give a simple yes/no as results to some of the questions.  Briefly explain why and how you obtain that result.

1. Now suppose a new worm break out. The feature of the worm is:

1)   It targets the TCP 8008 or UDP port 4004

2)    It contains the signature “03 0E FE CC A0” follow by “PASS : RECV” within the 20 bytes of the first one.

3)  The worm is coming from outside of our network (129.105.100.0/24).

Add a firewall rule to block that worm. Suppose the firewall use this kind of rule format:

| Action | Src | port | dest | port | flags | comment |
| --- | --- | --- | --- | --- | --- | --- |
| allow/block | IPsubnet, use * to refer any host | port number or * (refer any) | IPsubnet, use * to refer any host | port number or * (refer any) | flag can be TCP, UDP | The description of this rule |

Write firewall rules based on the above format to the Ditty worm traffic towards our network (129.105.100.0/24).

Hint: assume that we do not have benign traffic on those services which the ditty worm rely on to propagate.

2.  In this question, we explore some applications and limitations of a packet filtering firewall.  For each of the question, briefly explain

1) can stateless firewall be configured to defend against the attack and how?

2) if not, what about stateful firewall ?

3) if neither can, what about application-level proxy?

  - Can the firewall prevent an online password dictionary attack from the external network on the telnet port of an internal machine?

  - Can the firewall prevent a user on the external network from opening a window on an X server in the internal network?  Recall that by default an X server listens for connections on port 6000

  - Can the firewall block a virus embedded in an incoming email?

  - Can the firewall be used to block users on the internal network from browsing a specific external IP address?

  - Can the firewall prevent external users from exploiting a security bug in a CGI script on an internal web server (the web server is serving requests from the Internet)?